## Slide 1: STL-FM: Trajectory Planning Through STL-Guided Flow Matching
Imposing temporal requirements on a generative motion prior at inference time
Gawtam Chithra Ramesh
Master’s thesis defence, carried out at ABB Robotics
Examiner: Dimos V. Dimarogonas
Supervisors: Luzia Knödler, Shaohang Han, Matthew Lock and Jonathan Styrud
Notes: A robot learns its motion from demonstrations. This thesis imposes a requirement on that learned motion afterwards, at inference, without retraining.

## Slide 2: Adhesive bonding with an ABB YuMi
Motivation → Background → Method → Results → Conclusions
Photo and quote: ABB customer story,
GE Healthcare, Helsinki
A single-arm YuMi applies a bead of fast-setting glue
to a prototype part.
The part changes on a rapid schedule,
so the program changes with it.
“Even in half an hour, we can get some major changes done to the code.”
Notes: A real cell from ABB. At GE Healthcare in Helsinki a single-arm YuMi picks a prototype component from a jig, applies a bead of fast-setting glue that is hard to apply by hand, and returns the part. The prototypes change on a rapid schedule. The customer's own words: even in half an hour they can get major changes done to the code. Every change of the product or the process requires a change of the program. [ABB customer story, IRB 14050 at GE Healthcare]

## Slide 3: Current practice
Motivation → Background → Method → Results → Conclusions
Adhesive A
taught once, then replayed
time
open time
✓
run 1
✓
run 2, identical
✓
run 3, identical
Adhesive B, faster curing
same program
time
open time
✗
seated too late
✓
timing reprogrammed
Bead moved
same program
position
taught bead
bead now
✗
placed off the bead
✓
path reprogrammed
Each change in the product or the process requires a change in the code
The timing and the position are not stated explicitly, and the program encodes them only implicitly
Notes: How such a cell works today. The motion is taught or programmed once and replayed exactly, run after run, and every run seats the part inside the adhesive's open time. [Click] A faster-curing adhesive shortens the open time. The same program now seats the part too late. [Click] An engineer changes the timing in the code. [Click] The bead is laid at a different position. The same program places the part off the bead. [Click] An engineer changes the path in the code. [Click] Each change of product or process requires a code change, because the requirements, when to seat and where, are not stated explicitly, and the program encodes them only implicitly. [§1.1; ABB customer story]

## Slide 4: From programming to generation
Motivation → Background → Method → Results → Conclusions
Program
One motion, coded by hand
Imitate
One predicted motion for each state
Generate
Plausible samples, which a requirement stated after training accepts or rejects
zone stated after training
Notes: There are three ways to obtain the motion. One: program it. One motion, coded by hand, and every change is a code change, as on the previous slide. [Click] Two: record demonstrations instead, and train a network on them. Ordinary regression predicts the most likely motion for each state; it generalizes to states near the demonstrations, but it returns a single trajectory, and the same input returns the same trajectory every time. It also blends distinct demonstrated motions into an average. [Click] Three: a generative model represents the distribution of plausible motions, and two draws give two different, plausible trajectories. The method depends on this property, because selection by a requirement stated after training is possible only where alternatives exist. Here a zone stated after training rules out three samples and leaves five. [§3.3.1; ALVINN, Ross et al.; §1.4]

## Slide 5: Requirements that change after training
Motivation → Background → Method → Results → Conclusions
Notes: This slide states the timing explicitly. In a load-and-bond cell the robot seats a component on an adhesive bead. It must seat within the adhesive's open time, hold for a minimum duration, and keep clear of the operator's side. Left, samples of a model trained on demonstrations. The same samples satisfy the requirement for one adhesive and violate it for another. The window and the hold depend on the adhesive, so they can change after the demonstrations are recorded. [§1.1, eq. 1.1]

## Slide 6: Problem
Motivation → Background → Method → Results → Conclusions
Given demonstrations recorded before training and a requirement φ stated after it, generate a trajectory that is plausible under the demonstrations and satisfies φ, without retraining.
Training-time conditioning learns the requirement from paired data and can require retraining outside its distribution
Notes: A demonstration records the instant of seating, not the required window: it witnesses that the requirement can be satisfied without determining it. A model trained on demonstrations alone has no input for the requirement, so a sample can seat too late and still end on the housing, and a benchmark that judges the final state counts it as a success. [Click] The problem: given demonstrations recorded before training and a requirement stated after it, generate a trajectory that is plausible under the demonstrations and satisfies the requirement, without retraining. Training-time conditioning, such as TeLoGraF, learns the requirement from paired data and degrades outside its training distribution. [§1.1, §1.2, Problem 4.1]

## Slide 7: Aim and research questions
Motivation → Background → Method → Results → Conclusions
Aim
A method for imposing STL requirements on a trained generative model at inference time
The trained model is called the learned prior, because it provides the motion that the requirement does not specify
RQ1
What does a demonstration witnessing a requirement imply about that requirement?
RQ2
What does maximizing the robustness score alone determine about a trajectory?
Method
STL-FM, robustness guidance of the learned prior
Notes: The aim: a method for imposing STL requirements on a trained generative model at inference time. Two open questions concern the requirement itself rather than the performance of a planner: whether a demonstration determines the requirement, and whether the robustness score alone determines a trajectory. The first two contributions answer them by proof. The third contribution is the method, STL-FM, which guides the learned prior, an unconditional model trained once by flow matching, by the gradient of STL robustness at one constant strength, and which is evaluated experimentally. [§1.2, §1.3; Ch. 4, App. A; Ch. 5]

## Slide 8: Approach
Motivation → Background → Method → Results → Conclusions
Offline, once
Per requirement, at inference
Per instance
Demonstrations
Flow-matching training
Learned prior
STL requirement φ
Compiler
Robustness score ρ
Guided sampler
Plan
Execution
Notes: The trained model is called the learned prior, because it provides the motion the requirement does not specify. The prior is trained once, offline, on demonstrations. Each requirement is compiled into a robustness score at inference. The guided sampler combines the two into a plan, which a controller executes. The bar at the top of each slide shows the section. [§1.3, Fig. 5.1]

## Slide 9: Stating the requirement
Motivation → Background → Method → Results → Conclusions
Offline, once
Per requirement, at inference
Per instance
Demonstrations
Flow-matching training
Learned prior
STL requirement φ
Compiler
Robustness score ρ
Guided sampler
Plan
Execution
Notes: First, how the requirement is written and how it is scored.

## Slide 10: Signal Temporal Logic
Motivation → Background → Method → Results → Conclusions
Seat within [a, b], hold for d, avoid the operator zone
The requirement bounds when the part is seated and where the robot may not go
Evaluated fragment: predicates μ, negation, conjunction, bounded ◇ and ◻
Maler and Nickovic 2004
Notes: Signal Temporal Logic expresses time bounds over real-valued signals, such as a robot trajectory. [Click] Eventually, the diamond, means at some instant of its window. Always, the box, means at every instant. The requirement says: at some instant in [a, b] the part becomes seated and stays seated for d, and at every instant the robot stays out of the operator zone. [Click] The requirement bounds only the timing of the seating and the region to avoid. The grasp, the approach and the rest of the motion are hard to write as a formula and are learned from the demonstrations. Every requirement in this talk is built from a predicate, a margin function of the state; negation; conjunction; and these two bounded temporal operators. [§1.1, eq. 1.1; §3.2; Remark rem:fragment]

## Slide 11: Robustness
Motivation → Background → Method → Results → Conclusions
Guidance uses the surrogate at κ = 10. Satisfaction is always scored with the exact semantics.
Donzé and Maler 2010; Leung et al. 2021; Kapoor et al. 2025 (STLCG++)
Notes: Robustness replaces the Boolean verdict with a real number, defined by recursion over the formula. A predicate gives its margin h, negation changes the sign, conjunction and always take a minimum, eventually a maximum over its window. Soundness: a positive score certifies satisfaction. Below, the avoidance margin of one plan over time. The exact robustness is the minimum of the margin, a single witness instant; its gradient acts on that one instant alone. Log-sum-exp replaces max and min, and at sharpness kappa = 10 in the experiments it spreads the gradient over the neighbouring instants. The formula is compiled by recursion over its syntax tree into this differentiable score, with no learned component, so a new requirement requires only a new syntax tree. The smoothed score is sound only up to a margin, so satisfaction is always scored exactly. Implementation: stljax, the JAX library of STLCG++. [§3.2, def:robustness, eq:robustness-sound; §3.2.3, eq:logsumexp; §4.2, alg:build-rho, prop:smoothing-bias]

## Slide 12: Learning the prior
Motivation → Background → Method → Results → Conclusions
Offline, once
Per requirement, at inference
Per instance
Demonstrations
Flow-matching training
Learned prior
STL requirement φ
Compiler
Robustness score ρ
Guided sampler
Plan
Execution
Notes: Second, the learned prior that generates the motion.

## Slide 13: Flow matching
Motivation → Background → Method → Results → Conclusions
Training
Sampling
K = 64 Euler steps. The prior is unconditional, trained once on
demonstrations, and its only conditioning is the start state.
Lipman et al. 2023; Liu et al. 2022
Notes: [Click to play] A point of this space is a whole trajectory. Flow matching trains a velocity field v_theta by regression onto the straight-line target tau_1 minus tau_0, from noise to data. Sampling integrates the field from s = 0 to s = 1, here in K = 64 Euler steps. The density deforms from one Gaussian into two modes, two plausible behaviours, here passing a fixture on either side. The prior is unconditional, trained once on demonstrations, and its only conditioning is the start state. [§3.3, def:fm, eq:fm-loss, eq:fm-ode-bg, Fig. 3.1; §5.1.1]

## Slide 14: Generation from noise
Motivation → Background → Method → Results → Conclusions
Notes: [Click to play] Generation from noise, applied to a robot trajectory. This clip shows a diffusion model. Flow matching produces the same kind of result along straight-line paths. The prior used here is unconditional, trained once on demonstrations, and its only conditioning is the start state. [§3.3; §5.1.1]

## Slide 15: Related work
Motivation → Background → Method → Results → Conclusions
Training-time conditioning
TeLoGraF, Meng and Fan 2025
Decompose-and-stitch
ZSTP, Liu et al. 2025
Trajectory optimization
Kurtz and Lin 2021
Safe-set enforcement
SafeDiffuser, Xiao et al. 2023
Inference-time robustness guidance
CTG, Zhong et al. 2022
STL-FM
on a flow-matching prior
Overview figures reproduced from the cited papers
Notes: Previous work differs in where the requirement enters. Training-time conditioning, such as TeLoGraF, learns the requirement from paired data and degrades outside the conditioning distribution. Decompose-and-stitch, such as ZSTP, splits the formula into timed waypoints before generation and fixes each operator's timing in advance. Trajectory optimization uses robustness with a known dynamics model, specified by hand. Safe-set enforcement, such as SafeDiffuser, keeps samples in a time-invariant safe set, which expresses no dwell or order. STL-FM belongs to inference-time robustness guidance, with CTG. Unlike CTG, it guides a flow-matching prior, whose velocity is bounded, so one constant strength is well posed where diffusion needs a schedule. It also evaluates long-horizon dwell, sequence and avoidance, including nested operators. [Ch. 2, §2.7]

## Slide 16: Comparison of approaches
Motivation → Background → Method → Results → Conclusions
Approach
Requirement enters
Rest of the motion from
Property
Trajectory optimization
Kurtz and Lin 2021
cost or constraint, with a known dynamics model
dynamics model, costs and feasibility constraints
specified by hand
Control barrier functions
Lindemann and Dimarogonas 2019
time-varying barrier functions, quadratic program
dynamics model and control cost
boundedness conjoined to the requirement
Training-time conditioning
TeLoGraF, Meng and Fan 2025
training, from requirement–demonstration pairs
conditioned flow-matching model
degrades outside the conditioning distribution
Decompose-and-stitch
ZSTP, Liu et al. 2025
timed waypoints, before generation
pretrained diffusion model, between waypoints
timing of each operator fixed in advance
Safe-set enforcement
SafeDiffuser, Xiao et al. 2023
barrier invariance in each denoising step
diffusion model
time-invariant safe set, no temporal operators
Inference-time robustness guidance
CTG, Zhong et al. 2022
robustness gradient, during sampling
diffusion model
strength coupled to the noise level, no certificate
STL-FM
this thesis
robustness gradient at the predicted endpoint, during sampling
learned prior, trained by flow matching
one constant strength, no retraining, no certificate
Entries summarize the cited works
Notes: The table compares each approach by where the requirement enters and by what determines the rest of the motion. Trajectory optimization and control synthesis with barrier functions represent the requirement explicitly, as STL-FM does, and the dynamics model and costs determine what the score leaves free; the barrier-function formulation of Lindemann and Dimarogonas also conjoins a boundedness clause to the requirement, and later work extends it to disjunctions and nested operators. Training-time conditioning learns the requirement from requirement-demonstration pairs. Decompose-and-stitch fixes the timing of each operator before generation. Safe-set enforcement gives an invariance certificate, but for a time-invariant safe set. CTG shares the guidance mechanism, on a diffusion model. STL-FM takes the rest of the motion from a learned prior, at one constant strength, and gives no certificate; a barrier-based tracker could execute an STL-FM plan, which is future work. [Ch. 2: rw-modelbased, rw-guidance, rw-decompose, rw-conditioning, rw-constraints, positioning]

## Slide 17: Guiding the prior
Motivation → Background → Method → Results → Conclusions
Offline, once
Per requirement, at inference
Per instance
Demonstrations
Flow-matching training
Learned prior
STL requirement φ
Compiler
Robustness score ρ
Guided sampler
Plan
Execution
Notes: Third, the guided sampler that combines the learned prior with the robustness score.

## Slide 18: Guided velocity field
Motivation → Background → Method → Results → Conclusions
vθ(τ, s)
learned prior field
τ̂ = τ + (1 − s) vθ
predicted endpoint
ρφ(τ̂)
requirement score
γ Σ ‖pₜ₊₁ − 2pₜ + pₜ₋₁‖²
smoothness penalty
λ0 ≥ 0 is one constant strength for the whole flow; no component of the sampling loop is trained.
Notes: The sampler integrates the guided velocity from the same Gaussian start as the prior. [Click] The prior velocity moves the iterate toward trajectories likely under the learned prior, extrapolated to a predicted endpoint. [Click] The requirement is scored at that predicted endpoint, alongside a smoothness penalty, and their difference forms a penalized objective; its gradient is taken, masked to the position coordinates, and normalized to unit length, so lambda_0 is a step size that transfers across requirements. This is a soft realization of the constrained problem, not a solution with a certificate. [§4.3, eq:guided-velocity; §4.5, eq:smoothness-penalty, eq:grad-normalize]

## Slide 19: Guided sampler
Motivation → Background → Method → Results → Conclusions
For k = 0, …, K − 1 with s = kΔs, Δs = 1/K and K = 64, from τ ~ N(0, I) with the start state pinned
vθ(τ, s)
learned prior field
τ̂ = τ + (1 − s) vθ
predicted endpoint
ρφ(τ̂)
requirement score
γ Σ ‖pₜ₊₁ − 2pₜ + pₜ₋₁‖²
smoothness penalty
∇τ̂
autodiff
mask, normalize
unit direction
λ₀ ĝ Δs
guidance term
τ ← τ + Δs(vθ + λ₀ĝ), then re-pin
π₀(τ) = x_start, repeat K times
Early in the flow τ(s) is mostly noise, whereas τ̂(s) is the prior’s estimate of the finished trajectory; the gradient is taken with respect to it, not through the network.
The full sampler is in backup
Notes: One step of the sampler, continuing the dataflow from the previous slide. [Click] Autodiff takes the gradient of the penalized objective with respect to the predicted endpoint. [Click] It is masked to the position coordinates and normalized to unit length. [Click] That gives the guidance term, lambda_0 times the normalized gradient times the step size. [Click] It is added to the nominal prior increment, the sum is taken as one Euler step, and the start state is re-pinned; the loop repeats for K steps. Early in the flow the iterate is mostly noise, and the gradient of its robustness would point in a direction unrelated to any plausible trajectory; the predicted endpoint is the prior's running estimate of the finished trajectory instead. [§4.4, eq:predicted-endpoint; §4.7, alg:guided-ode]

## Slide 20: Evaluating the plans
Motivation → Background → Method → Results → Conclusions
Offline, once
Per requirement, at inference
Per instance
Demonstrations
Flow-matching training
Learned prior
STL requirement φ
Compiler
Robustness score ρ
Guided sampler
Plan
Execution
Notes: Finally, the evaluation: what the plans satisfy, and what their executions achieve.

## Slide 21: Experimental setup
Motivation → Background → Method → Results → Conclusions
Planar navigation
100 runs per class, plans only
Cube manipulation
10 runs per class, executed
Planner
Learned prior
Requirement
Endpoint pin
Endpoint-inpaint planner
✓
✓
STL-FM
✓
✓
STL Optimizer (no-prior)
✓
STL-FM with endpoint pin differs from STL-FM in satisfaction rate by at most 0.05 on any of the six classes (backup)
Notes: Two settings. Planar navigation: 100 runs per class on one fixed instance per class, plans only. Cube manipulation in OGBench: 10 runs per class on three classes, each plan executed in the simulator. Each baseline differs from STL-FM in one component. The endpoint-inpaint planner replaces the requirement by a pinned endpoint instead of the robustness gradient. The STL Optimizer (no-prior) keeps the requirement and removes the prior; it descends the violation penalty with a smoothness penalty and a velocity limit. A fourth planner, STL-FM with endpoint pin, differs from STL-FM in satisfaction rate by at most 0.05 on any of the six classes. [§5.1.2-5.1.3, tab:families, tab:planners]

## Slide 22: Six requirement classes
Motivation → Background → Method → Results → Conclusions
Reach
STL-FM
STL Optimizer
Nested reach-and-dwell
STL-FM
STL Optimizer
Recurrence
STL-FM
STL Optimizer
Sequence
STL-FM
STL Optimizer
Sequence with avoidance
STL-FM
STL Optimizer
Composite
STL-FM
STL Optimizer
One learned prior and one constant strength λ0 are used for all six requirement classes
Notes: The same prior and the same lambda_0 for all six classes. A new requirement requires only a new syntax tree. Satisfaction rates of STL-FM: reach 0.96, nested reach-and-dwell 1.00, recurrence 0.98, sequence 0.89, sequence with avoidance 0.89, composite 0.78. The STL Optimizer satisfies every class on every run, so the panels show plan shape rather than a satisfaction gap; on sequence and sequence with avoidance its plans leave the arena (next slide). A sweep of one requirement's own parameters is future work, so this does not test adaptation to a changed parameter. If asked about roughness: on nested reach-and-dwell 47 percent of turns exceed a right angle. [tab:families; tab:openloop; §4.2; §6.1; §7.2]

## Slide 23: Logic satisfaction and time to satisfaction
Motivation → Background → Method → Results → Conclusions
STL-FM satisfies most classes at comparable rates and plans 5 to 25 times faster
Notes: Over 100 runs per class. The endpoint-inpaint planner satisfies reach on every run and no other class on any run: the pin fixes the end, and the prior generates the remainder of the trajectory, which contains no dwell, order or avoidance. STL-FM satisfies the five history-dependent classes at 0.78 to 1.00. The STL Optimizer satisfies every class on every run, so satisfaction alone does not separate it from STL-FM. Below, estimated wall-clock time to first satisfaction, assuming every step of a planner takes the same time: 0.10 to 1.07 seconds for STL-FM against 0.83 to 6.75 for the optimizer, and on every class the optimizer is the later. A whole plan takes 0.42 to 1.15 seconds for STL-FM and 5.67 to 28.22 seconds for the optimizer. In the cube study STL-FM plans in 0.24 seconds and the optimizer in 0.96. In the kitchen STL-FM plans in 0.25 seconds under both priors, against 0.16 and 0.21 seconds for the unguided prior. Times are medians over 20 separate timing runs per class on a laptop GPU, an NVIDIA RTX A500, without recording the robustness at every step. A repeated measurement of the cube and kitchen times was up to 20 percent slower, with the same order of the planners. [tab:openloop; §5.2.3, tab:anytime; §5.3; §5.4; app:anytime; §6.1]

## Slide 24: Arena excursion
Motivation → Background → Method → Results → Conclusions
STL Optimizer
STL-FM
Sequence with avoidance, 25 of 100 plans per planner, arena clipped at its edge
Every plan of the STL Optimizer for sequence with avoidance leaves the arena
Notes: The STL Optimizer removes the prior and optimizes robustness directly. It descends the violation penalty with a smoothness penalty and a velocity limit. It satisfies every requirement class on every run. On sequence with avoidance every one of its plans leaves the arena, at a median largest coordinate of 10.27 against a half-width of 5.0. The excursion lies at steps 31 to 63, which no reach window covers. Deleting the avoidance conjuncts leaves the plans outside the arena, so the avoidance conjuncts do not cause the excursion. Its plans also leave the arena on sequence. Plans that use the prior cross the arena edge in at most 4 of 100 runs per class, by a small margin. [§5.1.3; §5.2.2; §6.1; app:noobs-ablation]

## Slide 25: Underdetermination by robustness
Motivation → Background → Method → Results → Conclusions
At most m of 64 to 256 waypoints determine the score, with m between 1 and 5
Robustness alone does not determine a trajectory (backup)
Notes: Robustness is computed from a few predicate evaluations combined by min and max. A formula with m predicate occurrences is determined by at most m waypoints, and m is between 1 and 5 here, against horizons of 64 to 256. Under the exact semantics the gradient is zero at every other waypoint, and the score is flat along a subspace of dimension at least (H - m) d. At steps that only avoidance constrains, the set of maximizers is unbounded. A planner guided by robustness therefore needs a component besides the requirement to determine the rest of the trajectory. Here that is the learned prior. Its contribution is measured, not assumed, because the prior does not meet the idealized conditions of the theorem in backup. [Contribution 2; §4.1.1; prop:sparse-gradient, thm:prior-resolves, prop:no-maximizer; rem:prior-idealization]

## Slide 26: Cube manipulation
Motivation → Background → Method → Results → Conclusions
Sequence requirement
Grasp the cube within 20 steps,
place it between steps 20 and 100
pick, the effector within 5 cm of the cube
place, the cube within 4 cm of the target, the environment’s tolerance
STL-FM plan, executed
STL-FM completes 10 of 30 executions, the STL Optimizer none
Notes: OGBench single cube. The prior generates the effector and the cube position over 128 steps, so the requirement and the environment's success criterion refer to the same cube. Place is a 4 cm ball about the target, the environment's own tolerance; pick holds when the effector is within 5 cm of the cube. [Click to play] A proportional controller tracks the effector and a gripper state machine follows the plan. STL-FM completes 10 of 30 runs, the STL Optimizer none. The endpoint-inpaint planner completes 1. [§5.3, tab:closedloop]

## Slide 27: Logic satisfaction and task success
Motivation → Background → Method → Results → Conclusions
Logic satisfaction and task success each occur without the other
Notes: Left, pooled over the three classes. Right, STL-FM per class. On nested reach-and-dwell STL-FM satisfies the requirement in 1 of 10 runs and completes the task in 9. The requirement constrains the grasp and the placement to hold over windows that close by step 30, whereas success requires only that the cube arrive. On sequence it satisfies 10 of 10 and completes 1. A requirement written on the generated variables constrains only those variables. The kitchen study shows the same gap more strongly (backup). [tab:closedloop, §6.2]

## Slide 28: Conclusions
Motivation → Background → Method → Results → Conclusions
RQ1
What does a demonstration witnessing a requirement imply about that requirement?
A demonstration witnesses a requirement without determining it, so the requirement is stated separately from the demonstrations.
RQ2
What does maximizing the robustness score alone determine about a trajectory?
The robustness score alone does not determine a trajectory. Its gradient depends on at most m waypoints, and its maximizers are unbounded where only avoidance applies. Without the prior, plans for the sequencing requirements leave the arena, and the planned cube moves without contact.
Method
STL-FM guides the learned prior at one constant strength, without retraining
STL-FM satisfies the dwell, sequence and avoidance requirements at rates of 0.78 to 1.00 per class and completes 10 of 30 cube executions, against none for the STL Optimizer.
Logic satisfaction and task success do not coincide. A requirement constrains only the variables the prior generates.
Notes: Back to the two questions. RQ1: a demonstration witnesses a requirement without determining it, so the requirement is stated as a formula and the demonstrations provide plausibility. RQ2: the robustness score alone does not determine a trajectory; its gradient acts on a few waypoints and its maximizers are unbounded where only avoidance applies. The learned prior provides the rest of the trajectory, as the navigation excursion and the cube carry gap show, and its contribution is not smoothness. The method: STL-FM guides the learned prior at one constant strength, without retraining, and covers nested and recurrent operators. Finally, satisfying the requirement on the plan is not completing the task: a requirement written on the generated variables constrains only those variables. STL-FM is a soft realization without a certificate. [§7.1; §6.1-6.3]

## Slide 29: Future work
Motivation → Background → Method → Results → Conclusions
1.
A differentiable dynamics model
so that a requirement can constrain contact and object pose
2.
Execution on the physical platform
plans for the GoFA door task, executed and scored on the robot
3.
A sweep of a requirement’s parameters
the same prior under changed windows and dwell times
4.
A barrier-filtered controller for execution
for an execution-time guarantee
Kitchen study, planned against executed
robustness (backup)
Notes: First, a differentiable dynamics or world model, so that a requirement can be written on contact, an object's pose or a hinge angle and constrain the executed behaviour. In the kitchen study under the complete-v2 prior every plan satisfies the requirement, and no execution does. Second, completion of the physical study: the GoFA prior is trained and the requirement compiled, but no plan has been executed. Third, a sweep of a requirement's own parameters with the prior held fixed, such as the open time or the dwell, which tests adaptation without retraining directly. Fourth, a barrier-filtered controller paired with the planner, for an execution-time guarantee. [§7.2; §2.6]

## Slide 31: Supplementary material
Answers to likely questions

## Slide 32: Plausible samples that violate the requirement
Notes: Backup for the problem slide. The demonstrations record the instant of seating. Samples of the learned prior can satisfy the window, seat too late, or release too early, and still end with the component on the housing. [§1.1, Fig. 1.1(b)]

## Slide 33: Requirements witnessed by one demonstration
A trajectory τ⋆ witnesses a requirement φ if it satisfies φ, that is, if τ⋆ lies in the satisfaction set 𝒮φ. Two requirements are equivalent if they have the same satisfaction set.
Any one trajectory witnesses uncountably many inequivalent requirements.
Their satisfaction sets form strictly increasing chains, from {τ⋆}, “do exactly this”, to the whole trajectory space 𝒯, “do anything”.
Consequently, no map from a single demonstration to a requirement is determined by the demonstration.
This answers RQ1. Witnessing constrains membership in a satisfaction set but does not determine which requirement was intended, and the requirement is stated separately from the demonstrations, as an STL formula.
Notes: This result answers RQ1. Any trajectory witnesses uncountably many requirements, ordered from 'do exactly this' to 'do anything', so no map from one demonstration to a requirement is determined by its argument. The chains already contain standard STL formulae, from a tight ball at every step to a tautology. The requirement is therefore stated, not inferred. [App. A, def:requirement, prop:witness-underdetermines]

## Slide 34: Sparsity of the robustness gradient
The result concerns a formula φ with m predicate occurrences, scored with the exact semantics at a trajectory τ where every min and max selection is unique.
Near τ the score depends on at most m waypoints, the active set 𝒜(τ).
The gradient is zero at every other waypoint, and the score is constant along a subspace N(τ) whose dimension in the position coordinates is at least (H − m)d.
Gradient ascent on the score leaves every coordinate in N(τ) at its initial value for as long as the active set is unchanged.
Here H is the horizon, d the dimension of the position coordinates, and πt the waypoint at step t.
In the experiments m lies between 1 and 5, against horizons of 64 to 256.
Notes: The first half of RQ2. Under the exact semantics the gradient is supported on at most m active waypoints, and the score is flat along a subspace of dimension at least (H - m) d. Under the smooth surrogate the gradient at the other waypoints is not zero, but it is suppressed exponentially in their robustness deficit. [App. A, prop:sparse-gradient, lem:smooth-concentration]

## Slide 35: Maximizers of a reach requirement
The reach requirement φ holds if the position lies within a ball of radius r about c at some step of [a, b].
Its largest score r is attained by every trajectory that is at c at some step of [a, b], whatever it does at the other steps.
The maximizing set 𝒪φ is therefore a union of affine subspaces, each of dimension (H − 1)d in the position coordinates.
It contains trajectories of arbitrarily large velocity and acceleration, and no rule internal to ρφ selects among them.
Maximality of the score implies nothing about plausibility.
Notes: For a reach requirement the maximizers include trajectories of arbitrarily large velocity. This is why guidance uses a penalized objective with a smoothness term rather than the score alone. [App. A, prop:spurious-maxima, eq:optimal-set; §4.5]

## Slide 36: Unbounded maximizers under avoidance
The predicate μ is an unsafe ball of radius r about c.
For the pure safety requirement ◻[0,H−1] ¬μ the score is unbounded above, so no maximizer exists.
With at least one reach conjunct the supremum is finite and attained.
At a step covered only by avoidance conjuncts, displacing the waypoint of a maximizer far from every unsafe centre leaves the score unchanged, so the set of maximizers is unbounded.
In neither case does the requirement bound the trajectory.
The coordinates that the requirement leaves free are determined by a component other than the requirement, in STL-FM the learned prior.
Notes: The second half of RQ2. Pure safety has no maximizer. With a reach conjunct the maximizers exist but are unbounded at time indices covered only by avoidance. In neither case does the requirement bound the trajectory. Control-synthesis formulations obtain the bound from the dynamics and costs, or conjoin a boundedness clause (Lindemann and Dimarogonas 2019). If asked about the STL Optimizer: it minimizes the violation penalty rather than ascending the score, so for it the result says only that no term of the requirement returns those coordinates to any region. [App. A, prop:no-maximizer, rem:violation-penalty; §2.2]

## Slide 37: Maximization over plausible trajectories
The plausible trajectories are idealized as a compact C1 submanifold ℳ of the trajectory space 𝒯, and the score is maximized on ℳ only.
Existence. The maximum is attained on ℳ, even where the unconstrained supremum is unattained or infinite, as for pure safety. Compactness of ℳ provides the bound that the requirement lacks.
Determinacy. For a generic embedding of ℳ the maximizers on ℳ are isolated, except where ℳ is tangent to the flat directions. In 𝒯 they are not isolated, as the sparsity and reach results show.
Plausibility. Every constrained maximizer lies in ℳ, so the implausible maximizers of a reach requirement are excluded whenever they lie off ℳ.
The learned prior satisfies neither hypothesis, so whether it provides the bound is measured in the experiments, not assumed.
Notes: Under idealized conditions, a compact manifold of plausible trajectories, the constrained problem attains its maximum and its maximizers are isolated. The learned prior satisfies neither hypothesis. A flow-matching sampler has support on the whole trajectory space, and the guided sampler realizes a soft penalty rather than the hard constraint. The contribution of the prior is therefore measured in the experiments, not assumed. [App. A, eq:constrained-problem, thm:prior-resolves, rem:prior-idealization]

## Slide 38: Constant guidance strength
Both terms are of the same bounded order at every flow time, so the ratio of guidance to prior is Θ(λ0)
and a constant λ0 is well posed without a schedule. λ0 = 50 in navigation and cube, without retuning.
On a diffusion substrate the guidance weight is coupled to the noise schedule,
λ(t) ∝ σtk with k ∈ {1, 2}.
Notes: Why one constant strength is well posed. The diffusion score grows like 1 over sigma_t squared as the noise vanishes, so a constant guidance weight has an influence that varies with the noise level, and diffusion guidance needs a schedule. Under the straight-line path the flow-matching target is tau_1 minus tau_0, of order one at every flow time, and the conditioned gradient has unit norm, so the guided velocity is bounded uniformly in s. One lambda_0 therefore has the same meaning throughout the flow. The claim is that a constant is well posed, not that it suffices in every setting. The same lambda_0 = 50 is used in navigation and cube without retuning. [eq:tweedie; §3.3; §4.6, eq:guided-bounded; tab:diffusion-vs-fm]

## Slide 39: Compilation and smoothing bias
A formula is compiled by a post-order traversal of its syntax tree, with no learned component.
A predicate returns its margin h at every step, and negation changes the sign.
Conjunction and always return smin, disjunction and eventually smax, and until a nested combination of both.
Over n arguments the surrogate lies within log n / κ of the exact extremum, so the compiled score converges to the exact score as κ grows.
At finite κ a compiled score above Lκ−1 log n implies satisfaction, where L is the depth of the syntax tree and n the largest arity of its nodes.
Guidance uses κ = 10, and satisfaction is always scored with the exact semantics.
Notes: The compilation is a post-order traversal of the syntax tree with no learned component. Smoothing replaces min and max by log-sum-exp. The bias is bounded by log n over kappa per node, and soundness is recovered exactly as kappa grows. kappa = 10 in the experiments, and satisfaction is scored with the exact semantics. [§4.2, alg:build-rho, prop:smoothing-bias]

## Slide 40: Steps of the guided sampler
The sampler takes the requirement score ρφ, the start state, the prior field vθ, the guidance strength λ0, the smoothness weight γ and the number of steps K.
1. τ is drawn from 𝒩(0, I), and its start state is pinned.
2. At each step k = 0, …, K − 1, with s = kΔs and Δs = 1/K, the prior velocity vθ(τ, s) is evaluated.
3. The predicted endpoint τ̂ is formed from the straight-line path.
4. The gradient g of the penalized objective is taken at τ̂, masked to the position coordinates and normalized.
5. The iterate is advanced by the prior step plus λ0 g Δs, and the start state is pinned again.
An optional clamp on the guidance increment is part of the sampler and is off in all reported runs.
Notes: The sampler in full. The predicted endpoint, the penalized requirement gradient, masking and normalization, the constant-strength update and the re-pinned start state are the steps of the guided-sampler slide. The optional clamp is off in all reported runs. [§4.7, alg:guided-ode]

## Slide 41: Reproducing the STL Optimizer
Removes the learned prior and optimizes the robustness score directly, instead of sampling from a trained generative model
Controls, not states
A free control sequence u, one 2D step per time index, starts from small random noise
Single-integrator dynamics
p[t+1] = p[t] + u[t]·Δt turns the controls into the trajectory that gets scored
Same compiled score
The requirement is scored by the masked, differentiable ρφ that STL-FM's guidance also uses (stljax / STLCG++)
Violation objective, no prior
Plain gradient descent on max(0, −ρφ); a finite-difference smoothness penalty and a velocity limit stand in for a learned prior
Budget
1,500–6,000 gradient steps, with the smoothing sharpness annealed from soft to sharp
The robustness engine is shared with STL-FM; the optimization built around it, single-integrator dynamics and the violation penalty, is a standard direct-optimization baseline, not something STLCG++ itself proposes.
Notes: How the STL Optimizer is actually computed, since it is named for what it scores rather than for how it works. Controls for a single integrator start as small random noise and are integrated into a trajectory at every gradient step, p of t plus 1 equals p of t plus u of t times delta t. That trajectory is scored by the same masked, differentiable robustness construction that stljax slash STLCG plus plus provides, and that STL-FM's own guidance term uses at every one of its integration steps. What differs is the objective: plain gradient descent on the violation penalty, max of zero and minus rho, with a hand-specified finite-difference smoothness penalty and a velocity limit taking the place of a learned prior, run for 1,500 to 6,000 steps with the log-sum-exp temperature annealed from soft to sharp. STLCG++ supplies the differentiable score; it does not propose this optimization design, which follows standard direct STL trajectory optimization (Belta and Vasile 2020). [§5.1.3]

## Slide 42: Navigation results, all four planners
Notes: The upper table gives satisfaction and mean robustness over 100 runs, and a star marks entries whose plans all leave the arena. Classes 1 to 6 are reach, nested reach-and-dwell, recurrence, sequence, sequence with avoidance and composite, and classes 7 to 10 are choice of target, choice of sequence, ordered visit and avoidance until reach. The lower table gives, per class, when each planner first satisfies the requirement and when it reaches its best robustness, as percentages of its budget, and the wall-clock plan time in seconds. STL-FM with endpoint pin differs from STL-FM by at most 0.05 on classes 1 to 6. [tab:openloop, tab:anytime; tab:families]

## Slide 43: Disjunction and until in navigation
Choice of target
◇μ₁ ∨ ◇μ₂
Choice of sequence
(◇μ₁ ∧ ◇μ₃) ∨ (◇μ₂ ∧ ◇μ₃)
Ordered visit
(¬μ₂ U μ₁) ∧ ◇μ₂
Avoidance until reach
(¬μ₃ ∧ ¬μ₄) U μ₁
Class
Endpoint-inpaint
STL-FM
STL-FM with pin
STL Optimizer
Plan time, STL-FM
Plan time, STL Optimizer
Choice of target
0.18
0.98
0.97
0.98
0.54 s
23.02 s
Choice of sequence
0.02
0.96
0.94
1.00†
0.75 s
22.92 s
Ordered visit
0.05
0.27
0.96
0.00†
5.72 s
–
Avoidance until reach
0.03
0.97
0.98
1.00†
4.69 s
32.03 s
Satisfaction over 100 runs, and plan time as a median over satisfying timing runs. † every plan leaves the arena. The STL Optimizer fails ordered visit at a local optimum of its objective
Notes: Added after the report: four navigation classes that use disjunction, choice of target and choice of sequence, and until, ordered visit and avoidance until reach, instantiated in the scene of the composite class. Panels show STL-FM, 25 of 100 runs. Under STL-FM the satisfied branch of a disjunction varies between runs. On choice of target 52 plans reach the distant target and 54 the near one, and on choice of sequence 14 take the branch through the first target and 84 the shorter branch, whereas the STL Optimizer always takes the branch through the near target. On ordered visit the first target lies 7.95 world units from the start and the second only 1.96, and the until operator forbids entering the second before the first. The STL Optimizer enters the near target first in every run. It fails at a local optimum and not because the instance is infeasible: the reach conjunct for the second target attains its value at an early waypoint near it, where its gradient is opposite to that of the until conjunct. Started from a plan that visits the first target first, it satisfies the instance, and with the second target's window moved to steps 31 to 63 it satisfies 19 of 20 runs. STL-FM satisfies 0.27 of runs, and STL-FM with endpoint pin 0.96, because the pinned final state satisfies the reach conjunct at the final index. The plan time of STL-FM on the two until classes, 4.7 and 5.7 s against 0.42 to 1.15 s elsewhere, is attributed to the compiled until, which is evaluated once for every end index of its window. Over all ten classes the estimated time to first satisfaction is 0.10 to 2.56 s for STL-FM and 0.83 to 7.29 s for the optimizer, excluding ordered visit. [§5.2.1, tab:openloop; §5.2.3, tab:anytime; app:ordered-visit, tab:ordered-visit; tab:families]

## Slide 44: Robustness against budget
Reach
Nested reach-and-dwell
Recurrence
Sequence
Sequence with avoidance
Composite
Notes: Robustness against progress through each planner's own budget, one panel per class, as the median over 100 runs with an interquartile band. The step axis is normalized per planner, so the comparison is of shape and not of cost. The dashed line is the satisfaction threshold. STL-FM reaches its largest robustness at 95 to 100 percent of its budget on the five history-dependent classes of the fragment, and the STL Optimizer at 10 to 57 percent on the classes it satisfies. [fig:anytime, fig:anytime-ext]

## Slide 45: Cube results, all three classes
Notes: In the table, sat is logic satisfaction on the plan, task is success on the rollout, and gap is the median carry gap in centimetres. Classes 2, 4 and 5 are nested reach-and-dwell, sequence and sequence with avoidance. The pooled row gives the medians quoted in the talk, 12.5 cm for the STL Optimizer and 6.9 cm for STL-FM. [tab:closedloop; tab:families]

## Slide 46: Kitchen study
Complete-v2 prior, unguided,
mean robustness of plan +0.23
and of execution −0.45, a fall of 0.68
against a margin of at most 0.3
Task success in 0 of 80 executions
Notes: D4RL kitchen. The requirement: open the microwave within steps 60 to 130, then move the kettle onto its burner within 140 to 230, with predicates on the fixtures' own state at the environment's tolerance. Two priors, complete-v2 and mixed, and two planners, the unguided prior and STL-FM, 20 runs each. Under complete-v2 every plan satisfies the requirement under both planners, because the demonstrations operate the fixtures in the required order, so guidance performs no selection. Under mixed, 6 of 20 without and 2 of 20 with guidance, no effect detected. No execution satisfies the requirement: the planned microwave crosses the threshold in every complete-v2 plan, the executed one in none. The prior generates the state, not the actions that produce it. [§5.4, tab:kitchen, §6.2]

## Slide 47: Physical platform
ABB GoFA CRB 15000,
five door-opening
demonstrations,
six joint angles and
the gripper state,
H = 128
No demonstration
satisfies the carry
requirement
Notes: ABB GoFA CRB 15000-12/1.27 with a parallel gripper. Five door-opening demonstrations of 894 to 1872 frames at 15 fps. The prior generates six joint angles and the gripper state over 128 steps. The carry requirement states that between grasp and release the tool must not rotate by more than 5 degrees about any axis, compiled through differentiable forward kinematics. No recorded demonstration satisfies it. Distance to the demonstration falls from 0.451 to 0.315 in the first 10,000 steps and then stays flat; only smoothness keeps improving; diversity falls about sevenfold, measured on four samples per checkpoint. No plan has been executed on the robot. The carry interval is a proxy read from the gripper trace. [§5.5, tab:gofa-checkpoints, §6.3]

## Slide 48: Roughness of guided plans
Trajectories
Median turn angle
Turns above 90°
Demonstrations
0.6°
2 %
Unguided prior, start pinned
6.4°
4 %
Unguided prior, both endpoints pinned
8.2°
7 %
STL-FM, nested reach-and-dwell
30.9°
47 %
STL-FM, recurrence
9.9°
STL-FM, composite
18.5 %
STL Optimizer, pooled
0.3°
The evaluation does not distinguish two explanations. Either the prior is undertrained, or guidance
moves iterates away from plausible trajectories faster than the prior moves them back. The evidence
for the contribution of the prior is the carry gap and the arena excursion.
Notes: Moving steps are steps longer than 0.05 world units. The prior does not reproduce the smoothness of its demonstrations, and guidance raises the turn angle on nested reach-and-dwell, where nearly half the turns exceed a right angle. On sequence and sequence with avoidance the guided plans are no rougher than the prior. The STL Optimizer is smoother than the demonstrations because of its hand-specified smoothness penalty. Two explanations remain open, and the evaluation does not distinguish them. The evidence for the contribution of the prior is the cube carry gap and the navigation excursion. [§5.2, §6.1]

## Slide 49: Limitations
Fixed requirement instances
every rate is measured on one instance per class
No certificate
the guided sampler is a soft realization, so it gives a rate, not a guarantee
Sampled-state semantics
robustness does not constrain the path between two sampled states
Requirement-neutral prior
a modelling assumption, although demonstrations can retain task structure
Reproducibility
runs with identical seeds agree on the satisfaction count in 27 of 28 cells and differ by one run in the other
Physical carry interval
a proxy read from the gripper trace, longer than the planning horizon
Notes: The limitations, one line each. [§6.3]