## Slide 1: STl-FM: STL-Guided Flow Matching
Gawtam Chithra Ramesh
Supervisors : Luzia Knödler, Shaohang Han, Matthew Lock and Jonathan Styrud

## Slide 2: Agenda
Problem definition – What are we trying to solve
Pre-requisites – Common concepts
Background – Overview of literature
Our work – How are we solving it
Results and Analysis – What does it say
Future Work – How this work can be extended

## Slide 3: Motivation

## Slide 4: Problem Definition
Industrial robot motion is usually programmed once and replayed. Under mass customisation every product variant needs reprogramming by an expert. Learning from demonstration lets a worker on the shop floor teach the task instead
A generative model is used because demonstrations of one task contain several valid motions, and a model that predicts a single motion averages them. [Thesis §1.1]

## Slide 6: Overview
Thesis topic : Data driven methods for control under STL specifications
Research Question :
  Can data driven methods leverage formal specifications of STL to generate robust and safe trajectories?
Agenda :
  Background of learning based method for robotic manipulation.
  How can STL be combined with them
  Why combining with STL make them better
  What have I done

## Slide 7: Pre-Requisites

## Slide 8: Signal Temporal Logic
A formal language
A precise way to say what the robot must do — and when.
“Glue the adhesive within 2 seconds
STL
F[0,2] (glue)
NATURAL LANGUAGE
01
Vocabulary (Predicates)
Replacing vague human words with strict physical boundaries.
02
Grammar (Logic and Time)
Connecting ideas to form complex, time-bound sequences.
03
Semantics (Robustness)
Evaluating not just if a rule is True/False, but how True/False.
Notes: So, what exactly is Signal Temporal Logic? The easiest way to understand it is to treat it exactly like a spoken language.
[Point to 01 Vocabulary] In any language, you start with basic words or simple facts. In English, you might say, 'I have to reach the office soon.' In STL, our vocabulary words are called predicates. But a robot doesn't understand vague words like 'soon' or 'fast'. Instead, we specify strict boundaries in the physical world that can be turned into math—like 'Time is less than 10 minutes' or 'Speed is under 2 meters per second'.
[Point to 02 Grammar] But individual words aren't enough. Like any other language, you need grammar rules to connect ideas and form complex sequences. We can't just shout the words 'in office' at a machine. We need a grammatical structure to say, 'I need to reach the office within 10 minutes.' STL gives us operators to map out exactly when things need to happen.
[Point to 03 Semantics] Lastly, we have semantics, the meaning of the sentence. Standard logic is Boolean; a sentence is just True or False. Did you reach the office on time, yes or no? But STL is much smarter. It allows us to not only say if something is True or False, but HOW true or HOW false it is. Did you reach the office with 5 minutes to spare, or did you slide in right at the buzzer? We call this continuous margin of safety Robustness, and it is what makes STL so powerful for robotics.

## Slide 9: Signal Temporal Logic
Formal Grammar

## Slide 10: Signal Temporal Logic
Semantics (Robustness)

## Slide 11: Signal Temporal Logic

## Slide 12: Signal Temporal Logic Evaluation: Robustness
Standard logic is Binary (Boolean): "Did you reach the goal?" (Yes / No)
STL Robustness () is Quantitative: "How deep inside the goal are you?" or "How far away are you?"
Spatial Robustness:
Positive Score (): Success!
    Meaning: You satisfied the rule. The number represents your "margin of safety" (e.g., means you are 15cm safely inside the goal zone).
  Negative Score (): Violation!
    Meaning: You broke the rule. The number represents your "distance to success" (e.g., means you need to move 40cm to reach the goal).
  Zero (): Exactly on the boundary.

## Slide 13: Signal Temporal Logic Evaluation: Robustness
Standard logic is Binary (Boolean): "Did you reach the goal?" (Yes / No)
STL Robustness () is Quantitative: "How deep inside the goal are you?" or "How far away are you?"
Spatial Robustness example :

## Slide 14: Flow Matching
“Generating” a trajectory
TRAINING
Many robot
Demonstrations
Diffusion
model learns
Motion
prior
"What good robot motion looks like"
INFERENCE
Random
noise
Iterative
refinement
Plausible
trajectory
Denoising steps
[ Diffusion denoising ]
Key insight: Task-agnostic motion prior -- knows how robots move, but not what the task is. Fast, flexible, multi-modal.

## Slide 15: Related works

## Slide 16: Learning to Manipulate
Generalizability and Safety
1
Imitation Learning
Learn from expert
demonstrations. Imitate the closest demonstration.
2
Reinforcement Learning
Learn from trial & error
with a reward signal
3
Generative Models
Learn trajectory distributions,
generate new ones
Observe picking an object 100 times,
Then mimic my picking
+ve (reward) if you pick,
-ve (penalty) if you collide, …
Understand robot and environment
Generate new scenarios and adapt
Notes: This is just to give a brief context, there are a lot more methods, each of them can be composed

## Slide 17: Learning to Manipulate
Generalizability and Safety
1
Imitation Learning
Pro : Best, if task is similar to data (In most cases it is)
Con : You need LOTS of data to generalize
2
Reinforcement Learning
Pro : No need data, agent generates data as it tries
Con : Reward engineering is complex
3
Generative Models
Hypothesis: Can we combine the flexibility of learned models with the formal guarantees of STL?
Observe picking an object 100 times,
Then mimic my picking
+ve reward if you pick,
-ve if you collide, etc …
Understand robot and environment
Generate new scenarios and adapt
Pro : Can generalize better
Con : Need data and conditioning
Data (task agnostic)
Data (STL-Trajectory pairs)
Generalizability
Safety??

## Slide 18: 4 Types of Related works …

## Slide 19: Method

## Slide 20: Guiding “generation" with STL
Flow matching
Diffusion Model
Generates candidate
trajectories
(motion prior)
STL Guidance
Robustness(ρ) modelled as CBFs steers
denoising toward
task satisfaction
Safe Trajectory
Task-satisfying,
formally verified
robot motion
No retraining
Swap the STL spec at inference
Formal guarantees
Separation of concerns
Motion intelligence + logical reasoning, decoupled
Control Barrier Functions (CBFs) enforce reachability and invariance constraints during the denoising process
Applied at generation, not baked in training (Less hallucination, More explainable)

## Slide 21: Experiments

## Slide 22: Results

## Slide 23: Discussions

## Slide 24: Future Work